By students Adil Arystanbek and Ganeshram Manisekaran Sujatha
2025.10.28
Battery Management System

---
A project to design a manufacturing ready Battery Management System:
- Capable of monitoring individual cell voltages of a 4 cell battery pack.
- Capable of monitoring the temperature of the battery pack.
- Capable of monitoring battery current.
- Control its charge and discharge.
Project basics

---
- All components have to be SMD.
- Temperature monitoring (via two sensors).
- Individual battery cell voltages measurement.
- MOSFET driven switch (both charging and discharging).
- Current measurement, including over current protection (10A).
- Plugin design to connect a NUCLEO-L15RE board to the BMS circuit.
- STM32 controller with over/under voltage per cell (2.5V min, 3.65V max. per cell),
  over/under temperature (charge: 0C to 40C and discharge: -20C to 40C).
Project specifications

---
- Version Control - GitHub.
- Circuit Simulation - LTspice.
- CAD - KiCAD.
Tools used

---
- Instrumentation Amplifier: 595-INA826AIDR
- Thermistor: 504-NRBE104J3435B2J
- MOSFET: 781-SI4116DY-E3
- Multiplexer: 595-TMUX1204DQAR
- Zener diode: 78-MMSZ4683-HE3_A-08
- Connector: 737-RS2BE-20-G-SMT, 437-8018700240002101, 649-1012938090202ALF
- Resistors: 708-RNCE0805BTE10K0, 667-ERJ-UP6D1600V, 603-PU2512FKNP50R01L
Components

---
- Battery = 9 Amps, 12.8 V, 111.6 W.
- Instrumentation Amp = 200 uA ~ 2.56 mW.
- NMOS = 8.6 mOhm ~ 0.6966 W.
- MUX = 10 nA ~ 128 nW.
- MCU(at highest possible mode of operation) = 84 uA ~ 277.2 uW
Power Efficiency / Parasitic Efficiency: 99.37%
Power Efficiency

---
AISLER.
- EU based, German.
- Fast delivery.
- Accepts KiCAD files.
Manufacturer choice

---
- Arduino plugin done through Morpho pins.
- No 90 degree angles present for the tracks.
- 1 mm and 0.5 mm track sizes used.
- No ICs were used.
- 2 layer PCB.
Extra design considerations

---
Delivered product

---
Soldering

---
Testing - Mistakes
Temperature measurement:
Design failure.
Current measurement:
Incorrect footprint.
Voltage measurement:
Bad choice of a component.

---
Testing - Fixes

---
Questions & Answers
section